## Slide 1: MATLAB
An Introduction

## Slide 2
Matlab
  one of many computing platforms we could use in this course.
  Others:
    Excel (with VBA)
    Mathematica
    MathCad
    Maple
    Handheld Calculator

## Slide 3: Matlab Advantages
Easily handles arrays
Efficient calculator
Good graphics
Built in structured programming language

## Slide 4: Matlab Disadvantages
Expensive
Large and slow to load
Command driven – not intuitive
Not readily available

## Slide 5: Use It
To Open
  Double click icon or an existing Matlab file
Has three interface windows or GUI’s
  Command Window – opens first by default
  Graphics Window
  Edit Window

## Slide 6: Command Window
Has four panes by default
  Command
  Command History
  File Directory
  Workspace

## Slide 7
Command Window
Workspace
File Directory
Command History

## Slide 8: Command Window
Enter commands in the Command Window
Can use as a simple calculator
  Without an assignment, results assigned to variable ”ans” by default
Can instead assign values to variables
  Use Assignment command “ =“
  NOTE: Names are case-sensitive
  Matlab creates proper type and saves to memory
  Puts the variable and its value into the workspace
  Results are automatically echoed – can shut off with ; at end of the command line

## Slide 9: Format Command
Controls how numbers are displayed – does not affect the value stored or the calculation precision
>> format ‘type’
  Possible types
    short (default) – four decimals displayed
    long – fifteen decimals displayed
    short e – exponential with four decimals
    long e – exponential with fifteen decimals
    short eng – engineering with four decimals
    long eng – engineering with fifteen decimals

## Slide 10: Arrays
Array – an organized collection or set of numbers
  Vector – one dimensional array – either a row or a column
  Matrix – two dimensional array
to enter
  use “ [ “ followed by elements and closed by “ ] “
  separate elements by a space
  separate rows by a ; or return

## Slide 11: Colon “ : “ Operator
Can be used as a wild card or short cut in creating arrays
Try it with: x = 5:2:21 or x=-10:5

## Slide 12: Math Operations
Matlab uses the standard operators
  +
  -
  *
  /
  ^
Note: Matlab automatically uses matrix operations by default. If a variable is an array you must have proper dimensions or you get an error
Element by element operations done only if an operator is preceded by a “ . “

## Slide 13: Built-In Functions
wide array of math functions are built-in
typical notation – sqrt( ), cos( ), abs( ), and many more
Help and definitions
  help > Function Browser (shift + F1)
  gives definitions, help and examples

## Slide 14: Some Useful Functions
zeros(n) – creates n x n matrix of zeros
zeros(n,m) – creates n x m matrix of zeros
ones(n) or ones(n,m) – same for matrices of all ones
eye(n) – creates n x n identity matrix
linspace(x1, x2, n) – creates linear array of n elements starting with x1 and ending with x2
  If n is omitted – default is 100 elements

## Slide 15: Graphics
basic plotting command
  plot(x,y) – creates graph of y(x)
    x = vector of x values
    y = vector of corresponding y values
    both must be of same dimension
formatting graphs
  grid or grid minor
  xlabel(‘ text ‘), ylabel(‘ text ‘)
  title(‘ text’)

## Slide 16: Try It – Free-Falling Object
Evaluate the solution (in m/s) given by:
  For t = 12 seconds
  Use
    m=68.1 kg
    g = 9.81 m/s^2
    c = 0.25 kg/s
Then evaluate v(t) for t = 0 to 25 seconds
  Plot v(t), label axis and add title
  Do in MSWord, put in header and footer, convert to pdf, and submit to practice dropbox.
Fd = c v2
mg